## Slide 1: MRI WW ADNI 2017
Mayo
Cliff Jack
Bret Borowski
Matt Bernstein
Arvin Forghanian-Arani
Jeff Gunter
Dave Jones
Kejal Kantarci
Rob Reid
Denise Reyes
Matt Senjem
Kaely Thostenson
Prashanthi Vemuri
Chad Ward
Funded MRI Investigators
Charlie DeCarli – UCD
Nick Fox – UCL
Duygu Tosun – SFVA
Paul Thompson – USC
Paul Yuskevich - Penn
Danielle Harvey – biostats
MR company scientists
Dan Rettmann (Mayo) – GE
Pete Kollasch (Mayo)/Gunnar Kruger (MGH) – Siemens
Yansong Zhao (BU) - Philips

## Slide 2: ADNI 3 protocol all 3T, all 8 sequences in all subjects (where possible)
3D T1 volume
3D FLAIR
T2* GRE
ASL – 3 possible sequences depending on model
TF-fMRI - advanced and basic versions
Field map
dMRI - advanced and basic versions
Coronal high resolution T2

## Slide 3: 3D T1: Change from ADNI 2 to 3
ADNI 2
  Unaccelerated and 2x accelerated
  all platforms
ADNI 3
  2x accelerated
  All platforms
  Slight resolution improvement – 1mm cubed

## Slide 4: FLAIR: Change from ADNI 2 to 3
ADNI 2
  all platforms
  2D FLAIR
  1x1x5 mm
ADNI 3
  all platforms
  3D FLAIR
  1x1x2 mm

## Slide 5: T2*GRE: Change from ADNI 2 to 3
None
All platforms
Hi res coronal: Change from ADNI 2 to 3
ADNI 2
  One vendor
ADNI 3
  Minor tune up to parameters
  all platforms

## Slide 6: ASL: Change from ADNI 2 to 3
ADNI 2
  One vendor – Siemens 2D PASL
ADNI 3
  all platforms (but must have license)
  3D pCASL : GE >15 & Philips 5.3
  3D PASL : Siemens VD & VE
  2D PASL: Siemens VB, Philips 3X and 5.1
  Upgrade schedule
    Siemens 3D pCASL ?

## Slide 7: dMRI : change from ADNI 2 to 3
  ADNI 2 - single vendor, single b=1000 shell
  ADNI 3 – all platforms, advanced or basic
  basic – single b=1000 shell
  advanced, HCP-like: b=500, 1000, 2000; 3X SMS, 6/8 PF
    Better FA/MD
    Enable NODDI, tractography, cortical hub to hub connectivity , multi tissue compartments
  Custom gradient direction set – posted LONI
Compatibility – derive equivalent of basic single b=1000 shell in every subject at no time penalty

## Slide 8: TF-fMRI: change from ADNI 2 to 3
ADNI 2 – single vendor, ~ 3 sec TR
ADNI 3 – all platforms, advanced or basic
  basic – 10 minute, ~3 sec TR
  advanced, HCP-like – 10 min, 600msTR, 8x SMS
    More precise measure of time series (temporal resolution)
    Less noisy node to node, ICA, graph theory measures
    Time varying connectivity metrics
  Compatibly advanced and basic  derived basic equivalent

## Slide 9: dMRI and TF-fMRI – requirements for advanced
32 or 64 channel head coil
multi band (SMS)
  Siemens product VE11C plus SMS license
  Philips 5.3 – initial roll out
  GE DV 26 – 2017 only dMRI; fMRI SMS?
Consequently, almost all ADNI 3 have started with basic and sites will step up to advanced as systems are upgraded

## Slide 10: Link to ADNI 3 protocol PDFs: http://adni.loni.usc.edu/methods/documents/mri-protocols/

## Slide 11: ADNI-3 MRI Protocols Posters
AIC: IC-P-137 Saturday, 12:15-13:30
(Poster #18496)
AAIC: P4-242 Wednesday, 12:00-13:00
(Poster # 16551)
Posted to http://adni.loni.usc.edu/methods/documents/mri-protocols/
General overview – Jeff Gunter PhD
Diffusion MRI – Rob Reid PhD
AAIC: P3-09 Tuesday, 12:00-13:00
(Poster # 327)